## Slide 1: Software Development Guide
<number>

## Slide 2: Selection of Target Platform
<number>
Manage Client
VB.NET
C#.NET
Native Client
C++
Web
Application
Client
Application
Selection
Selection of
Development Language
Selection

## Slide 3: Manage and Native
<number>
Manage Client
Visual Studio 2005 or 2008
Language：VB.NET
C#.NET
Native Client
Visual Studio 2005 or 2008
Language：C++
Managed Client
  Executes Managed Code on Common Language Runtime
  Can exploit .NET applications and XML Web service.
  Can develop application software by Drag & Drop operation visually.
  Can improve productivity by Custom Control.
Native Client
  Executes Computer Binary Code.
  Can derive functions and performance of the devices at most.
  Can optimize performance and process speed.

## Slide 4: Development Tool for Native Client
<number>
Required Tools for Native Application Development
  From Microsoft (Software)
    Visual Studio 2005 + SP1 (or 2008 + SP1)
    Microsoft Windows Mobile 6 Professional SDK
    Microsoft Windows Mobile 6.5.3 Developer Tool Kit
    Microsoft Windows Mobile 6.5 Developer Tool Kit (If necessary)
    ActiveSync 4.5 (or later)
    Microsoft Windows Mobile Device Center 6.1 (for Windows Vista)
    * Please download tools listed above from Microsoft Home Page.
  From CASIO (Software)
    CASIO IT-300 BDK (Basic Development Kit)
    * Please download tools listed above from Microsoft Home Page.
    http://www2.casio.co.jp/system_en/pa/PADealer/
  From CASIO (Hardware)
    IT-300 including HA-J65US (USB and charging unit) and USB cable

## Slide 5: Steps of Software Development 1
<number>
Visual Studio 2005 (Visual C++)

## Slide 6: Steps of Software Development 2
<number>
Visual Studio 2005 (Visual C++)

## Slide 7: Steps of Software Development 2
<number>
Visual Studio 2005 (Visual C++)

## Slide 8: Steps of Software Development 2
<number>
Visual Studio 2005 (Visual C++)

## Slide 9: Steps of Software Development 3
<number>
Note: Before building the program, it is necessary to connect the IT-300 to the PC by
Active Sync. Active Sync can be download from Microsoft Web site.
USB
Visual Studio 2005 (Visual C++)
The application program will be downloaded to the IT-300 after compiling.
If breakpoints are set, the program stops at each point while the IT-300 is connected as remote connection.

## Slide 10: Managed Code Development Tool
<number>
Required Tools for Managed code Development
  From Microsoft (Software)
    Visual Studio 2005 + SP1 (or 2008 + SP1)
    Microsoft Windows Mobile 6 Professional SDK
    Microsoft Windows Mobile 6.5.3 Developer Tool Kit
    Microsoft Windows Mobile 6.5 Developer Tool Kit (If necessary)
    ActiveSync 4.5 (or later)
    Microsoft Windows Mobile Device Center 6.1 (for Windows Vista)
    * Please download tools listed above from Microsoft Home Page.
  From CASIO (Software)
    CASIO IT-300 BDK (Basic Development Kit)
    * Please download tools listed above from Microsoft Home Page.
    http://www2.casio.co.jp/system_en/pa/PADealer/
  From CASIO (Hardware)
    IT-300 including HA-J65US (USB and charging unit) and USB cable

## Slide 11: Steps of Software Development 1
<number>
Visual Studio 2005
Start up Visual Studio 2005 and create new project, then select VB or VC#
VB
VC#

## Slide 12: Steps of Software Development 2
USB
<number>
Start Debugging
Visual Studio 2005
IT-300
Select “Windows Mobile 6 Professional Device”

## Slide 13: Usage of Common Device Control Library
<number>
1. Visual C++
2. VB.NET

## Slide 14: Visual C++ Step 1
<number>
Currently we have released the following Common Device Control Library
Lib files
Header files
CAB files
C:\Program Files\CASIO\MBSys\CAB
C:\Program Files\CASIO\MBSys\INCLUDE
C:\Program Files\CASIO\MBSys\LIB\ARMV4I

## Slide 15: Visual C++ Step 2
<number>
Try to use “SysGetModelName” function in system library
First, you append
“#include “SystemLib.h” sentence to use System library.

## Slide 16: Visual C++ Step 3
<number>
Then you should append “SysGetModelName” function sentence like this.

## Slide 17: Visual C++ Step 4
<number>
Header file path setting
Then you set header file path setting in this “Property Pages”.

## Slide 18: Visual C++ Step 5
<number>
Library file path setting
Then you set library file path setting in this “Property Pages”.

## Slide 19: Visual C++ Step 6
<number>
Library file path setting
Then you set library file name in this “Property Pages”.

## Slide 20: Visual C++ Step 7
<number>
Deploying and debugging
IT-300

## Slide 21: VB.NET Step 1
<number>
Currently we have released the following Common Device Control Class Library
DLL files
CAB files
C:\Program Files\CASIO\MBSys\CAB
C:\Program Files\CASIO\MBSys\WindowsCE

## Slide 22: VB.NET Step 2
Add Reference operation
<number>
First of all, you append “SystemLibnet” into
References in Solution Explorer.

## Slide 23: VB.NET Step 3
<number>
Coding
Write code which is using system library function

## Slide 24: VB.NET Step 4
<number>
Deploying and debugging

## Slide 25: Usage of Emulator
<number>
1. Visual C++
2. VB.NET
3. Device control
    Bluetooth

## Slide 26: Emulator (Visual C++)
<number>
To start emulation, run “IT-300” from Start menu “CASIO Device Emulation”
Notes: <number>

## Slide 27: Emulator (Visual C++)
<number>
Open “Device Emulator Manager” from Visual Studio 2005 menu.

## Slide 28: Emulator (Visual C++)
<number>
Select “DMA” in ActiveSync setting.
Select “Cradle” then ActiveSync connection will be established.

## Slide 29: Emulator (Visual C++)
<number>

## Slide 30: Emulator (VB.NET)
<number>
To start emulation, run “IT-300” from Start menu “CASIO Device Emulation”

## Slide 31: Emulator (VB.NET)
<number>
Open “Device Emulator Manager” from Visual Studio 2005 menu.

## Slide 32: Emulator (VB.NET)
<number>
Select “DMA” in ActiveSync setting.
Select “Cradle” then ActiveSync connection will be established.

## Slide 33: Emulator (VB.NET)
<number>

## Slide 34: Device control
You can control the following device on this emulator.
  Bluetooth
<number>
When you refer “Storage Card” folder in this emulator,
There are some these devices folder.

## Slide 35: Device control
<number>
Bluetooth
When you use Bluetooth control library on emulator, emulator devices will
Response the setting parameter or data.
And when you change these file detail, you can get your expected value.